## Slide 1: PROJECT-2 OAD for SensorTag Hardware CSE 6349-Fall 2015
Sneha Kadam
Shwetabh Srivastava
Karthikeyan Rajamani
Saroj Panda

## Slide 2: Project Description
TI’s SensorTag hardware comes pre-programmed with TI’s default factory firmware(SensorTag project).
In order to change the firmware, the SensorTag needs to be programmed using TI’s debugger or using the over the air(OAD) feature.
Our project uses the second scheme for programming the SensorTag.
We have developed an Android application which connects with the SensorTag over BLE and gives an option to the user to program it.
Once the user connects to the tag, he can download a new firmware by clicking on the “Start Programming” button.
After the new program gets downloaded, the SensorTag resets itself and runs with the new updated firmware.

## Slide 3: IDE’s and devices used
SensorTag –CC2650STK from Texas Instruments
XDS110 USB debugger
Samsung Galaxy S4(API-19)
Android Studio -1.4.1
IAR embedded workbench (ARM tool chain)
Code Composer Studio- Version: 6.1.1.00022

## Slide 4: Work done
Developed Android Application SensPhy, which allows the user to upgrade the firmware over the air (OAD)
SensPhy allows selecting default image identified or custom image for upgrade.
Created various SimpleBlePeripheral Images(.bin) using CCS,IAR & Python2.7 following the TI OAD-2.1 documentation guidelines.

## Slide 5: Problems And the Solutions
BluetoothGatt.setCharacteristicNotification(Charatcteristic,true) enables only local notifications. We had to write the descriptor BluetoothGatt.writeDescriptor(#descriptor) to get notified from the SensorTag remotely.
After writing a characteristic to the Sensortag, we get Oncharacteristicchanged callback,then we wrote the next program block. This sequential writing of blocks resulted in a total programming time of 12 minutes. We reduced the time to 4 minutes by running two threads, one for writing characteristics & other for queuing up program block.
.bin file creation
  Adding version number bricked the Device (Ex:OAD_Image_Full_v_1.20)
  We wrote the x,bin created as per the OAD TI guidelines & the tag became undetectable.
  We had SimpleBLEperipheral firmware OAD enabled , when programmed via the App it returned Gatt error code=1(failure)
  We created a BIM+Stack+Image bin & was not recognized by the App when programmed.

## Slide 6: Future Work
SimpleBleperipheral OAD enabled should be resolved for the OAD GATT error on the App. Enabling a new image to be programmed
The memory architecture & Vectors of the OAD image-A & image-B, inconsistencies in documentation has to be studied leading to clear understanding.

## Slide 7: References
https://git.ti.com/sensortag-20-android/sensortag-20-android/trees/master
http://processors.wiki.ti.com/index.php/CC2650_SensorTag_User's_Guide#When_connected
http://www.compel.ru/wordpress/wp-content/uploads/2015/08/CC2640-BLE-OAD-Users-Guide.pdf
http://stackoverflow.com/questions/17910322/android-ble-api-gatt-notification-not-received
http://stackoverflow.com/questions/23367726/android-ble-cant-receive-gatt-characteristic-notification-from-device
https://newcircle.com/s/post/1553/bluetooth_smart_le_android_tutorial
http://www.cumulations.com/blogs/7/Doing-firmware-upgrade-over-BLE-in-Android
https://www.safaribooksonline.com/library/view/getting-started-with/9781491900550/ch04.html
http://www.ti.com/lit/ug/swru393/swru393.pdf
http://www.ti.com/ww/en/wireless_connectivity/sensortag2015/?INTC=SensorTag&HQS=sensortag

## Slide 8: Thank you!